## Slide 1: BAYESIAN SYSTEM IDENTIFICATION AND PREDICTIVE ALGORITHMS IN WAVEFRONT SENSING AND CONTROL FOR EXOPLANET IMAGING
Internship Supervisors
Laurent PUEYO
Colin NORMAN
ENS Supervisor
Mohamed ABBAS-TURKI

## Slide 2: SUMMARY
Context
1 |
Methods
2 |
Results
3 |
Conclusion
4 |

## Slide 3: SUMMARY
Context
1 |
Methods
2 |
Results
3 |
Conclusion
4 |

## Slide 4
CONTEXT Direct Imaging of Exoplanets
The key scientific objective of future NASA astrophysics flagship missions is to find out if there is life elsewhere in our universe, through two major projects:
Habitable Exoplanet Observatory (HabEx)
Large UV/Optical/Infrared Surveyor (LUVOIR)
Scientific goals:
SEARCH FOR EARTH-LIKE PLANETS
Are there terrestrial planets with similar atmospheres?
SEARCH FOR LIFE
Does extraterrestrial life exist?
SEARCH FOR SOLAR SYSTEM ROLE IN THE UNIVERSE
What does it have of typical or atypical?

## Slide 5
CONTEXT Reinventing the Optical System
WAVEFRONT SENSING AND CONTROL (WFS&C) ALGORITHMS
OPTICAL INSTRUMENTS
These methods have never been sent to space yet
  What we have now
  What we want in 2030
From a block diagram perspective:
Design of optical instruments and
WFS&C algorithms go hand-in-hand

## Slide 6
CONTEXT Model of the Optical System
Linearity assumption:
Deformable Mirrors have a small actuation
Coronagraph has a linear influence
Noise on the phase of the electric field:
We have and need to estimate to correct its phase

## Slide 7
CONTEXT Most Important Metrics
    The observation time
    Computation time
    Lost time on the telescope
    The contrast
    Given by the relation How faint of a signal can we detect?
Finally, the two main metrics we use are:
We want them as small as possible

## Slide 8: SUMMARY
Context
1 |
Methods
2 |
Results
3 |
Conclusion
4 |

## Slide 9
Currently: estimation of from
Currently: estimation of 𝑬 from 𝑰
Statistical methods
Future: estimation of from
Future: estimation of 𝑬 from 𝑬
Statistical methods
METHODS Introduction to the Estimation Problem
How to estimate the electric field ?
The intensity is the square modulus of the electric field

## Slide 10
At pixel :
METHODS State of the Art – Pairwise Estimation
Idea: Choose a set of probe functions that will be applied to DMs and measure resulting intensity patterns
Use measured intensities along with forward model to construct system of equations and solve for real and imaginary part of field at each pixel in dark zone
  Pairwise Estimation
  Only used method currently
Probing creates a huge loss in observation time
Need for new algorithms

## Slide 11
METHODS Predictive Filter – Presentation
Matrix-vector representation
Classical least squares estimator
Can be regularized if necessary
Temporal representation
=
Find that minimizes the average distance between prediction and
a-posteriori measurements
Estimate at the next step
Filter
History of past wavefronts

## Slide 12
METHODS Origin of the Algorithm
Previous application: Control of the atmospheric turbulence on ground telescopes
MATHEMATICAL UNDERSTANDING
Time series analysis
Singular values decomposition
Regularized least squares
VALIDATION OF THE ALGORITHM
Python & packages
Jupyter notebooks
Analysis of relevant metrics
IMPLEMENTATION ON THE TESTBED
Version control (Git)
Integrated development environment (PyCharm)
Progression of the internship

## Slide 13
METHODS Predictive Filter – Advantages
EOFs
Best estimator in the least squares sense
Allows the incorporation of different types of data
Possible to estimate at every pixel
Possible to estimate 𝑬 at every pixel
Don’t need a model for the data
EOFs
Best estimator in the least squares sense
Allows the incorporation of different types of data
Don’t need a model for the data
  Use past estimated by Pairwise to predict the next

## Slide 14: SUMMARY
Context
1 |
Methods
2 |
Results
3 |
Conclusion
4 |

## Slide 15
RESULTS Dark Hole Creation
Idea: Create a zone of very low contrast, the dark hole
DARK HOLE CREATION
Pairwise estimation
Control algorithm
DARK HOLE MAINTENANCE
Mix Pairwise & Filter
Control algorithm
Control
Estimation

## Slide 16
RESULTS Algorithm Implementation on the Testbed Simulator
Contrast is similar to the lowest values we can currently achieve
Contrast vs Iterations
    Metric What is the dark hole maintenance contrast using the predictive filter?
  Desired contrast to reach for space missions is

## Slide 17
RESULTS Algorithm Implementation on the Testbed
MODULE CREATION
- Using Python & HciPy
- Includes accommodating functions (initialization, SVD truncature, etc…)
IMPLEMENTATION ON THE TESTBED
- Using Version Control
- Can directly call the functions in the main branch

## Slide 18
RESULTS Algorithm Implementation on the Testbed
Huge reduction in computing time
No need for probes anymore
Time difference between Predictive filter and Pairwise estimation
    Metric What is the gain in time with the predictive filter?
On a space telescope, an estimated
of the time will be allocated for probing

## Slide 19: SUMMARY
Context
1 |
Methods
2 |
Results
3 |
Conclusion
4 |

## Slide 20
CONCLUSION Achievements
UNDERSTOOD
VALIDATED
IMPLEMENTED
FINE-TUNED
The algorithm has been:

## Slide 21
In the laboratory
CONCLUSION Impact
And elsewhere
EXPAND ON OTHER TESTBEDS
Princeton University
Goddard Space Flight Center
University of Arizona
OPEN-SOURCE DISTRIBUTION
Laboratory module « catkit » GitHub visibility went from private to public on September
ARTICLE IN PREPARATION
In collaboration with the University of California Santa Cruz
IMPLEMENTED ON THE TESTBED
Code is running on the laboratory testbed, which was the ultimate goal of the internship

## Slide 22
Thank you

## Slide 24
RESULTS Algorithm Validation – Algorithm in Practice (1)
Discussion on Training Set
1e-3, 80/5 (l,n)

## Slide 25
RESULTS Algorithm Validation – Algorithm in Practice (2)
Discussion on regularization
    Need to recompute filter frequently for now Find right value for the parameters

## Slide 26
APPENDIX Future Research
Find tradeoff between code architecture and optics architecture
Determine good filter parameters
Find right number of vectors in the training set
Find right value for the regularization
Determine optimal architecture
Which computation power do we have?
Study autocorrelation in history vectors
Study filter "breakpoint"
Research on optics and materials
Investigate segmented apertures
    What will future research focus on?